CapTouch I2C interface

Each board have mark with number.
Each board have it’s own I2C address.
Board number	I2C address
1	0x41
2	0x42
3	0x43
4	0x44
5	0x45
6	0x46

pi@sanchox-rpi3:~ $ i2cdetect -y 1
     0 1 2 3 4 5 6 7 8 9 a b c d e f
00: -- -- -- -- -- -- -- -- -- -- -- -- --
10: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
20: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
30: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
40: -- 41 42 43 44 45 46 -- -- -- -- -- -- -- -- --
50: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
60: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
70: -- -- -- -- -- -- -- --

Each board have set of registers with data for each capacitive element on board.
For this FW version available data:
- from 0x0 to 0x12 – uint16 values represents each capacitive element raw value
- from 0x20 to 0x32 – uint16 values represents each capacitive element filtered value (not usable because lack of threshold constants data)

Elements numbering example:
8	1	2
7	9	3
6	5	4